Burning sticks for Native American Flute

Dit is een fragment van de originele tekst van de voormalige verkoper van de sticks:

Burning Sticks by AHÕKEN were created for flute makers. Burning Sticks provide ease and accuracy. The burning tip is simply heated with a propane torch, gas flame or campfire. Burning eliminates the “break out” associated with drilling. These professional grade tools are machine manufactured out of high quality steel for precision accuracy. Each Stick offers hand protection with a comfortable ergonomic wooden handle. They are a total 9” long with the tip of each tool 5/8” long. Available in 2 sizes: Small (5/32-1/4”) and Medium (7/32-5/16”).

The undercut tool is invaluable for fine tuning. Achieve perfect tuning by undercutting the hole rather  than enlarging the hole size. This allows for a more accurate and comfortable playing flute. We use these tools here at the Custom Flute Shop and recommend them to all flute makers. Each tool comes with a full set of instructions and a protective case.

Small (Best for cane and bamboo) $15; Medium (The best all around tool) $15; Undercut tool $15

Dit zijn enkele foto’s  om je een idee te vormen (groter kan ik ze niet vinden):

Dit zijn de maten (heb ik geconverteerd) van de small en medium tools (ik vermoed 4 per set).

Small 		5/32 inch  tot   1/4 inch  =  4 mm  tot  6.35 mm (doorsnede uiteinde neem ik aan)

Medium 	7/32 inch  tot  5/16 inch =  5,6 mm  tot  7.9 mm

Lengte tools 	23 cm inclusief handvat

Lengte tip 	 16 mm

http://mdmetric.com/tech/cvtcht.htm ( voor conversie inch naar metriek)